## Slide 1: BITZER Compressor Nomenclature

## Slide 2: GSD 6 / 8 - Nomenclature
1 | 2 | 3 | 4 | 5,6,7,8 | 9 | 10 | 11 | 12 | 13 | 14
Model | Config. | Refrigerant | Series | Cooling Capacity | Oil | Application | Connection | Nominal Voltage | Motor Protection | Design Variable
G | S | D | 8 | 0385 | V | A | B | 4 | 3 | 2
Model:
G: Scroll
Configuration:
S: Single
T: Tandem
Y: Trio
Refrigerant:
D: HFC-410A
Capacity:
(kBtuh @ ARI)
6 Series
0120 (10t)
0137 (12t)
0154 (13t)
0182 (15t)
0235 (20t)
8 Series
0295 (25t)
0385 (32t)
0421 (35t)
0485 (40t)
Oil Charge:
V: PVE Oil
Series:
6: 6 Series
8: 8 Series
Application:
A: Air Cooled
W: Water Cooled (GSD8 only)
Connection:
B: Brazed
R: Rotalock (GSD8 only)
Voltage: (3Ph)
2: 208/230-60, 200/230-50
3: 380-60
4: 460-60, 400-50
5: 575-60, 500-50
Motor Protection:
- : Not defined
1: SE-E1 Module (115/230V) w/ Phase-Rotation monitor
2: SE-B2 Module (24VAC) Installed
3: SE-B3 Module (115/230V ) Standard
4: SE-E1 Module (24VAC) w/ Phase-Rotation monitor
5 : DGTS Installed
6: SE-E1 Module (115/230V) w/ DGTS installed
7: SE-B2 Module (24VAC) w/ DGTS installed
8: SE-B3 Module (115/230V ) w/ DGTS installed
9: SE-E1 Module (24VAC) w/ DGTS installed
Design Variable:
0: Original Design
1: w / Integral discharge check valve
2: design update

## Slide 3: ESH Scroll Series Nomenclature
1,2 | 3 | 4 | 5,6 | 7 | 8
Model | Config. | NH3 | Frame Size | Displ | Series
ES | H | 7 | 36 | Y | 4SU
Model:
ES: Standard
Configuration:
H: High Temperature
7:
Series
Displacement:
25,30,36,43
Voltage Code:
2SU: 208/230
4SU: 460
5SU: 575
Oil Type:
Y: POE
Blank: AB

## Slide 4: CSH.3, CSW, HS Screw Series Nomenclature
1,2 | 3 | 4,5 | 6 | 7 | 8,9,10 | 11 | 12
Model | Config. | Frame Size | Displ | Series | Motor HP | Oil | Motor Code
CS | W | 75 | 7 | 3 | 90 | Y* | 4PU
Model:
CS: Screw
HS: Screw
Configuration:
H: High Condensing
W: Low Condensing
K: Med/High Temp
N: Low Temp
Frame Size:
HS: 53/64/74/85 CS: 65/75/85/95
Displacement:
4..11
Series:
1,3
Code for
Motor Size:
90: Horsepower
Voltage: (3Ph) UL
2NU: 208-230/460 (HS53 Only)
1PU: 200-60 (HS/CS65/75)
2PU: 208/230-60 (HS/CS65/75/85)
3PU: 380-60 (HS/CS65/75/85)(CS95 3DU)
4PU: 460-60 (HS/CS65/75/85)(CS95 4DU)
5PU: 575-60 (HS/CS65/75/85)(CS95 5DU)
Oil Type:
Y: POE 170 Oil (CSH)
Y: POE 170L Oil (CSW)
Blank: POE 320 Oil (R22)
*Oil Charge/Type:
Y: CSH/CSW with HFC POE 170 Oil
Y: CSW with R134A POE 170L Oil
If No “Y” in model number: CSH/CSW with R22 POE 320 Oil

## Slide 5: CSV Screw Series Nomenclature
1,2 | 3 | 4 | 5 | 6 | 7,8 | 9 | 10 | 11
Model | Config. | Application | Displ | Series | Motor HP | Motor Type | Oil | Motor Code
CS | V | W | 2 | 5 | 90 | M* | Y | 4PU
Model:
CS: Screw
Configuration:
V: Variable Speed
Application Range:
H: Optimized air cooled chillers –
heat pump applications
W: Optimized water cooled chillers
Housing Size:
2..3
Motor*:
M: Permanent Magnet Motor
Inverter Size:
4…6
Motor Code:
4AU: 380..480 volt / 3 / 50-60Hz
4MU: 380..480 volt / 3 / 50-60Hz
Motor Size:
125, 160, 200
Oil Charge/Type:
Y: POE 170

## Slide 6: OS Screw Series Nomenclature
1,2 | 3 | 4,5 | 6 | 7 | 8
Model | Config. | Frame Size | Displ | Series | Design
OS | K | 74 | 6 | 1 | K
Model:
OS: Open Screw
Configuration:
N: Low Temperature
K: Med/High Temperature
Frame Size:
53,74,85
Displacement:
4..7
Series:
1
Design:
K: Direct Coupling
1,2 | 3 | 4 | 5,6 | 7 | 8 | 9
Model | Config. | NH3 | Frame Size | Displ | Series | Design
OS | N | A | 85 | 6 | 1 | K
Model:
OS: Open Screw
Configuration:
N: Low Temperature
K: Med/High Temperature
H: High Temperature (OS.A74)
A:
NH3 Design
Frame Size:
53,74,85,95
Series:
1; Standard
2: High Temp (OS.A74)
Design:
K: Direct Coupling
Displacement:
4..10

## Slide 7: Recip Series Nomenclature
1 | 2 | 3 | 4 | 5,6 | 7,8,9 | 10 | 11
Model | Config. |  | Lube | Motor HP | Voltage | Unloaders | Oil
4 | G | E | S | 30 | 2NU | 1* | D*
No. of Cylinders
2,4,6,8
Identification:
Bore and Stroke
Series:
Ecoline
Oil Lubrication:
S: Centrifugal CE1..CE4
Oil:
D: Dry
Y: POE
Motor Size:
30: Horsepower
Voltage: (3Ph) UL
2NU: 208/230-460
3PU: 380-60
4PU: 460-60
5PU: 575-60
Unloaders:
1..3
*Bitzer US Only
Inverter (not shown):
.F3: Inverter size

## Slide 8: ECOSTAR Series Nomenclature
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | - | 9 | 10 | 11
Model | Config. | Fans | Series | Comp. | HP | VFD | Oil | - | Future | Future | Future
LH | V | 7 | E | 4CE | 9 | F3 | Y | - | x | x | x
Model:
LH: Cond. Unit
Configuration:
V: Variable Speed
Fans:
5: 1 Fan
7: 2 Fan
Compressor:
Displacement
Horse Power:
Series:
E: ECOLINE
VFD:
F3 Only
Oil:
Y: BSE32
Notes: Standardize on the slide title and format (above the green line)
Title line 1 - same name and format as presentation title on first slide except at 28pt
Title line 2 - same name and format as heading on first slide except at 28pt
Standardize on format of Specific slide title (below green line)
Specific slide title more detialed (i.e. product offering, highlights, piping
or
Standardize on the slide title and format (above the green line)
Title line 1 - same name and format as presentation title on first slide except at 28pt
Title line 2 - Specific slide title more detialed (i.e. product offering, highlights, piping
Standardize on format of Specific slide title (below green line)
Eliminate completely or use only when necessary to provide even more details
Bullet point levels
Standardize on format (ie. no bold)
Should we us 18pt instead of 20pt for spacing issues?

## Slide 9: Varispeed Series Nomenclature
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Model | Config. | Series | Lube | Motor HP | Inverter | Oil | Motor Code
4 | V | E | S | 10 | F4 | Y | 4SU
No. of Cylinders
2,4
Identification:
Bore and Stroke
Series:
Ecoline
Oil Lubrication:
S: Centrifugal
Oil:
D: Dry
Y: POE
Motor Size:
3…20: Horsepower
Voltage:
2NU: 208/230-460
4SU: 460-60
Inverter:
3…4

## Slide 10: ACP Series Nomenclature
1,2,3 | 4,5,6,7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Model | Config. | Application | Qty | Config | Oil Cooling | Controller | Economizer | Starter Panel
SCP | 7472 | K | 2 | V | H | B | E | P
Model:
SCP: Screw Compressor Packages
ACP: Ammonia Compressor Packages
Size of Compressor Used:
5361, 7472, 8561
Unequal: “M”
(“SCP74M”)
Application Range:
N: Low temperature
K: Medium temperature
H: High temperature (74 series)
B: Booster application
Capacity Control Method:
V: Variable frequency
C: Capacity control (w/o VFD)
Controller:
B: With Controller
Oil Cooling Method:
H: Thermosiphon or Water/Brine via HX
L: Liquid Injection
Starter Panel:
P: Soft-Starter or
VFD Panel Included
Number of Compressors:
Economizer:
E: Economizer Heat Exchanger Included

## Slide 11: Motor Compressor Assembly Nomenclature
1,2,3 | 4,5,6,7 | 8 | 9 | 10 | 11 | 12 | 13
Model | Config. | Application | Qty | Horsepower | Voltage and Motor Type | Terminal Box | Variant
S | D | 7471 | K | 100 | 2 | L | A
Model:
S: Screw Compressor
R: Recip Compressor
Drive Type:
D: Direct Drive
B: Belt Drive (Recip Only)
Compressor Model:
Example: 5341…7471
Horsepower:
3 digits required
Controller:
B: With Controller
Voltage and Motor Type:
H:
Starter Panel:
P: Soft-Starter or
VFD Panel Included
Application Range:
N: Low temperature
K: Med/High temperature
H: High temperature
B: Booster application
Economizer:
E: Economizer Heat Exchanger Included